MR Inversion Recovery Calculation
Simulation and optimizing of
IR sequences using MatLab
Øystein B Gadmar & Wibeke Nordhøy

---
3D Fluid Attenuated Inversion Recovery
- One IR pulse, then a TI delay before readout
- 3D T2-weighted readout (SPACE/CUBE/VIEW)
- T1 weighting from IR counteracts the desired T2 contrast...

---
FLAIR – Fluid Attenuated Inv. Recovery
size 12{ alignc{ stack{ E rSub{size8{t}} `≝` e rSup{size8{-`{ t over ital"T1" }}} ~;~ M rSub{size8{t}} `=` M rSub{size8{0}} `-` left( M rSub{size8{0}} `-` M rSub{size8{1}} right) E rSub{size8{t}} {} # {} # bold{S} `≝` { M rSub{size8{ital"TI"}} } over { M rSub{size8{0}} } `=` 1 `-` left("1"`-`"-1"right) E rSub{size8{ital"TI"}} bold{ `=` underline{ 1 `-` 2E rSub{size8{ital"TI"}} } } {} # {} # downarrow {} # {} # S rSub{size8{0}}`=`0 ~drarrow~ E rSub{size8{ital"TI"}} `=` e rSup{size8{ -`{ ital"TI" over ital"T1" } }}`=`{ 1 over 2 } {} # {} # drarrow~ bold{ ital"TI" `=` underline{ ital"T1" `·` "ln"left( 2 right) } } {} # {} # {} # alignr size8{ital"Q.E.D."} } } }
TI
Inv.
CSF
WM/GM

---
“Simple” FLAIR
4200 × ln(2) = 2911

---
Our IR Calculator for MatLab
Git!

---
Notes On Noise
- S = Signal strength at TE
- C = Difference between SWML and SWM (usually)
- N = Noise ∝ sqrt(t)
- CNR = C/N ∝ t/sqrt(t) = sqrt(t)
- Contrast efficiency: CNR/t ∝ C/sqrt(TR)
- CNR/t – a good end point (but also look to SNR/t)

---
Realistic 3D FLAIR

---
“Vendor” 3D FLAIR w/ short TR???

---
“Vendor” 3D FLAIR w/ T2 Prep.!
Std. for further
comparison

---
T2 prep. – How?
- 90°x – [ 180°y ]n – -90°x to achieve spin lock
- T2P and inversion are interchangeable
- Pure T2 decay used for Mz preparation
- CSF hardly affected (long T2), but tissues relax much

---
IR-Calc (0th: In Real Time)
size 12{ alignc{ stack{ E rSub{size8{t}} `≝` e rSup{size8{-`{ t over ital"T1" }}} ~;~ M rSub{size8{t}} `=` M rSub{size8{0}} `-` left( M rSub{size8{0}} `-` M rSub{size8{1}} right) E rSub{size8{t}} {} # {} # { M rSub{size8{1}} } over { M rSub{size8{0}} } `=` 1`-`E rSub{size8{ left(ital"TR" - ital"TI"right) }} `=` 1`-`{ {E rSub{size8{ital"TR"}}} over {E rSub{size8{ital"TI"}}} } {} # {} # bold{S} `≝` { M rSub{size8{ital"TI"}} } over { M rSub{size8{0}} } `=` 1`-` left( 1+{ { M rSub{size8{1}} } over { M rSub{size8{0}} } } right)E rSub{size8{ital"TI"}} bold{ `=` {underline { left( 1+ital"E" rSub{size8{ital"TR"}} right) `-`left("1+1"right)E rSub{size8{ital"TI"}}} } } {} # {} # downarrow {} # {} # S rSub{size8{0}}`=`0 ~drarrow~ E rSub{size8{ital"TIn"}} `=` e rSup{size8{ -`{ ital"TIn" over ital "T1" } }} `=` { { 1+ital"E" rSub{size8{ital"TR"}} } over 2 } {} # {} # drarrow~ bold{ ital"TI" rSub{size8{n}} `=` underline{ ital"T1" left[`"ln"left( 2 right) `-`"ln"left( 1+ital"E" rSub{size8{ital"TR"}} right)` right ]`;~ E rSub{size8{ital"TR"}} `=` e rSup{size8{ -`{ ital"TR" over ital"T1" } }} } } {} # {} # {} # {} # alignr size8{"Q.E.D."} } } }
TI
TR – TI
M0
M1
MTI
-M1

---
IR-Calc (1st: Effective TR)
size 12{ alignc{ stack{ E rSub{size8{t}} `≝` e rSup{size8{-`{ t over ital"T1" }}} {} # {} # { M rSub{size8{1}} }over{ M rSub{size8{0}} } `=` 1`-`E rSub{size8{ left(ital"TR"- ital"TI" right) }} `=` 1`-`{ E rSub{size8{ital"TR"}} }over{ E rSub{size8{ital"TI"}} } ~;~ left( ital"TR" rightarrow ital"TR" rSub{size8{ital"eff"}} right) {} # {} # bold{S rSub{size8{0}}} `≝` { M rSub{size8{ital"TI"}} }over{M rSub{size8{0}} } `=` 1`-` left( 1+ { M rSub{size8{1}} }over{ M rSub{size8{0}} } right) E rSub{size8{ital"TI"}} bold{ `=` underline{ left( 1+ital"E" rSub{size8{ital"TR"}} right) `-` left("1+1"right) E rSub{size8{ital"TI"}} } } {} # {} # downarrow {} # {} # S rSub{size8{0}}`=`0 ~drarrow~ E rSub{size8{ital"TIn"}} `=` e rSup{size8{ -`{ ital"TIn" }over{ ital"T1" } }} `=` { 1+ital"E" rSub{size8{ital"TR"}} }over{ 2 } {} # {} # drarrow~ bold{ ital"TI" rSub{size8{n}} `=` underline{ ital"T1" left[ `"ln" left( 2 right) `-`"ln" left( 1+ital"E" rSub{size8{ital"TR"}} right)`right] `;~ E rSub{size8{ital"TR"}} `=` e rSup{size8{ -{ ital"TReff" }over{ ital"T1" } }} } } {} # {} # {} # {} # alignr size8{"Q.E.D."} } } }
TReff = TR – TRo
TI
TReff – TI
M0
M1
MTI
-M1

---
The efficiency of inversion efficiency?
~ 95% – 99%

---
IR-Calc (2nd: Inefficient Inversion)
size 12{ alignc{ stack{ E rSub{size8{t}} `≝` e rSup{size8{-`{ t over ital"T1" }}} ~;~ α `≝` -"cos" left( ital"FA" rSub{size8{ital"inv"}} right) {} # {} # { M rSub{size8{1}} }over{ M rSub{size8{0}} } `=` 1`-`E rSub{size8{ left(ital"TR"- ital"TI" right) }} `=` 1`-`{ E rSub{size8{ital"TR"}} }over{ E rSub{size8{ital"TI"}} } ~;~ left( ital"TR" rightarrow ital"TR" rSub{size8{ital"eff"}} right) {} # {} # bold{S rSub{size8{0}}} `≝` { M rSub{size8{ital"TI"}} }over{M rSub{size8{0}} } `=` 1`-` left( 1+ital"α" { M rSub{size8{1}} }over{ M rSub{size8{0}} } right) E rSub{size8{ital"TI"}} bold{ `=` underline{ left( 1+ital"αE" rSub{size8{ital"TR"}} right) `-` left( 1+ital"α" right) E rSub{size8{ital"TI"}} }} {} # {} # downarrow {} # {} # S rSub{size8{0}}`=`0 ~drarrow~ E rSub{size8{ital"TIn"}} `=` e rSup{size8{ -`{ ital"TIn" }over{ ital"T1" } }} `=` { 1+ital"αE" rSub{size8{ital"TR"}} }over{ 1+ital"α" } {} # {} # drarrow~ bold{ ital"TI" rSub{size8{n}} `=` underline{ ital"T1" left[ `"ln" left( 1+ital"α" right)`-`"ln" left( 1+ital"αE" rSub{size8{ital"TR"}} right)` right] } } {} # {} # {} # {} # alignr size8{"Q.E.D."} } } }
TRo
TI
TReff – TI
M0
M1
MTI
-αM1

---
IR-Calc (3rd: Be T2 Prepared!)
size 12{ alignc{ stack{ E rSub{size8{t}} `≝` e rSup{size8{-`{ t over ital"T1" }}} ~;~ α `≝` -"cos" left( ital"FA" rSub{size8{ital"inv"}} right) ~;~ E rSub{size8{ital"T2P"}} `≝` e rSup{size8{-`{ital"T2P"}over{ital"T2"} }} {} # {} # { M rSub{size8{1}} }over{ M rSub{size8{0}} } `=` 1`-`E rSub{size8{ left(ital"TR"- ital"TI" right) }} `=` 1`-`{ E rSub{size8{ital"TR"}} }over{ E rSub{size8{ital"TI"}} } ~;~ left( ital"TR" rightarrow ital"TR" rSub{size8{ital"eff"}} right) {} # {} # bold{S rSub{size8{0}}} `≝` { M rSub{size8{ital"TI"}} }over{M rSub{size8{0}} } `=` 1`-` left( 1+ital"α" { M rSub{size8{1}} }over{ M rSub{size8{0}} } right) E rSub{size8{ital"TI"}} bold{ `=` underline{ left( 1+ital"αE" rSub{size8{ital"TR"}} right)`-` left( 1+ital"α" right) E rSub{size8{ital"TI"}} } } {} # {} # downarrow {} # {} # S rSub{size8{0}}`=`0 ~drarrow~ E rSub{size8{ital"TIn"}} `=` e rSup{size8{ -`{ ital"TIn" }over{ ital"T1" } }} `=` { 1+ital"αE" rSub{size8{ital"TR"}} }over{ 1+ital"α" } {} # {} # drarrow~ ital"TI" rSub{size8{n}} `=` underline{ ital"T1" left[ `"ln" left( 1+ital"α" right)`-`"ln" left( 1+ital"αE" rSub{size8{ital"TR"}} right)` right] } {} # {} # downarrow {} # {} # α rightarrow ital"αE" rSub{size8{ital"T2P"}} ~drarrow~ bold{ ital"TI" rSub{size8{n}} `=` underline{ ital"T1" left[ `"ln" left( 1+ital"αE" rSub{size8{ital"T2P"}} right)`-`"ln" left( 1+ital"αE" rSub{size8{ital"T2P"}} E rSub{size8{ital"TR"}} right)` right] } } {} # {} # alignr size8{ital"Q.E.D."} } } }
TReff = TR – TRo – T2P
TRo
TI
TReff – TI
M0
M1
MTI
-αM1
!?

---
3D TSE readout – How?
- Complex flip angle sweep to preserve magnetization
- Complex profile ordering to avoid artefacts/blurring
- TEeff estimated; much shorter than zero crossing time!
- Contrast mainly T2 – some T1?!
- Mz probably used up over TRo?
- We’re working to understand it…!

---
TR 6 s – “One up” on the vendor

---
TR 9 s – FLAIR And Back Again?!
Acceleration?!

---
Fluid Attenuated IR … by how much?
“Images that computers like”
TE ↓ ?

---
DIR-WM – A Pulse Too Far?
CNR/t bad. Better at low TE – at the cost of WML–GM CNR

---
Dual IR: Two for the price of WM (and SNR)
TE ↓ !?
(& CNR)

---
T1-nulled DIR – A New Hope

---
T1-nulled DIR – How?
Find the TI1/TI2 pair that null the difference between the DIR signal for T1 times of WM and WML
Find the T1 that is nulled at these TI1/TI2
WM will be brighter, but SNR/CNR better
Optimal TE will be free of T1 effects
[Madhuranthakam et al, Mag Res Med 2012 67(1):81-88]

---
DIR-Calc (Inversion juggling)
size 12{ alignc{ stack{ { M rSub{size8{1}} }over{ M rSub{size8{0}} } `=` 1`-`E rSub{size8{ left( ital"TR"-ital"TI" rSub{1} right) }} `=` 1`-`{ E rSub{size8{ital"TR"}} }over{ E rSub{size8{ital"TI" rSub{1} }} } ~;~ left( ital"TR" rightarrow ital"TR" rSub{size8{ital"eff"}} right) {} # {} # { M rSub{size8{2}} }over{ M rSub{size8{0}} } `=` 1`-`left( 1`+`α { M rSub{size8{1}} }over{ M rSub{size8{0}} } right) E rSub{size8{ left( ital"TI" rSub{1} - ital"TI" rSub{size 8{2} } right) }} `=` { 1 }over{ E rSub{size8{ital"TI" rSub{2}}} } left[`E rSub{size8{ital"TI" rSub{2}}} +ital"αE" rSub{size8{ital"TR"}}`-`left( 1+ital"α" right) E rSub{size8{ital"TI" rSub{1}}}`right] {} # {} # S rSub{size8{0}} `≝` { M rSub{size8{ital"TI"}} }over{ M rSub{size8{0}} } `=` 1`-` left( 1+ital"α" { M rSub{size8{2}} }over{ M rSub{size8{0}} } right) E rSub{size8{ital"TI" rSub{2}} } {} # {} # bold{ S rSub{size8{0}} `=` underline{ 1`-`left( 1+ital"α" right) E rSub{size8{ital"TI" rSub{2}}}`+`ital"α" left( 1+ital"α" right) E rSub{size8{ital"TI" rSub{1}}}`-` ital"α" rSup{size8{2}} ital"E" rSub{size8{ital"TR"}} } } {} # {} # downarrow {} # {} # S rSub{size8{0}} `=` 0 ~drarrow~ {} # {} # bold{ ital"TI" rSub{size8{ital"1n"}} `=` underline{ ital"T1"`"ln" left(`left[` ital"α" left( 1+ital"α" right)`right] `/` left[`"-1"`+`left( 1+ital"α" right) E rSub{size8{ital"TI" rSub{2}}}`+` ital"α" rSup{size8{2}} ital"E" rSub{size8{ital"TR"}}`right]`right) } } {} # {} # {} # alignr size8{ital"Q.E.D."} } } }
TI1
M0
M1
M2
-αM2
-αM1
TI1 – TI2

---
DIR-Calc (Oh My T2P... version)
size 12{ alignc{ stack{ { M rSub{size8{1}} }over{ M rSub{size8{0}} } `=` 1`-`E rSub{size8{ left( ital"TR"-ital"TI" rSub{1} right) }} `=` 1`-`{ E rSub{size8{ital"TR"}} }over{ E rSub{size8{ital"TI" rSub{1} }} } ~;~ left( ital"TR" rightarrow ital"TR" rSub{size8{ital"eff"}} right) ~;~ ital "β"`"≝"`"αE" rSub{size8{ital"T2P"}} {} # {} # { M rSub{size8{2}} }over{ M rSub{size8{0}} } `=` 1`-`left( 1`+`β { M rSub{size8{1}} }over{ M rSub{size8{0}} } right) E rSub{size8{ left( ital"TI" rSub{1} - ital"TI" rSub{size 8{2} } right) }} `=` { 1 }over{ E rSub{size8{ital"TI" rSub{2}}} } left[`E rSub{size8{ital"TI" rSub{2}}} +ital"βE" rSub{size8{ital"TR"}}`-`left( 1+ital"β" right) E rSub{size8{ital"TI" rSub{1}}}`right] {} # {} # S rSub{size8{0}} `≝` { M rSub{size8{ital"TI"}} }over{ M rSub{size8{0}} } `=` 1`-` left( 1+ital"α" { M rSub{size8{2}} }over{ M rSub{size8{0}} } right) E rSub{size8{ital"TI" rSub{2}} } {} # {} # bold{ S rSub{size8{0}} `=` underline{ 1`-`left( 1+ital"α" right) E rSub{size8{ital"TI" rSub{2}}}`+`ital"α" left( 1+ital"β" right) E rSub{size8{ital"TI" rSub{1}}}`-`ital"αβE" rSub{size8{ital"TR"}} } } {} # {} # downarrow {} # {} # S rSub { size 8{0} } `=`0~ drarrow ~ {} # {} # bold{ ital"TI" rSub{size8{ital"1n"}} `=` underline{ ital"T1"`"ln" left(`left[` ital"α" left( 1+ital"β" right)`right] `/` left[`"-1"`+`left( 1+ital"α" right) E rSub{size8{ital"TI" rSub{2}}}`+`ital"αβE" rSub{size8{ital"TR"}}`right]`right) } } {} # {} # {} # alignr size8{ital"Q.E.D."} } } }
TI1
M0
M1
M2
-αM2
-βM1
TI1 – TI2

---
TrueT2-DIR – From Zero To Hero!

---
TrueT2-DIR – From Zero To Hero!

---
TrueT2-DIR vs FLAIR images
TrueT2
FLAIR
CNR/t at least as good as FLAIR; better WML–GM CNR?!

---
DIR 4 Dummies!
Accessible spreadsheet tools, based on simulation regressions

---
DIR 4 Dummies!?
Measuring WM and WML T1 values w/ MP2RAGE MRI

---
DIR 4 Dummies???
Good regressions may be hard
to get right, but…
Their results are easy to use!